## Slide 1: Abbey Line Timetable Options

## Slide 2: Timetable Options
Option 1 - 45 minute frequency (no change – as now)
Same frequency as current
Performance risk due to minimum turnrounds
Connections vary by hour due to 45 minute interval interfacing with hourly mainline service
Option 2 – hourly frequency
More robust due to increased turnrounds
Possibility of slightly later services without exceeding current mileage
Standard connections throughout the day
Easy timetable for customers to understand
Option 3 - Hybrid
45 minute frequency during the peak, hourly off peak
Maintains 4 round trips before 9:30am
Leisure travellers get benefit of simplified timetable

## Slide 3: Context – why consider change?
Current round trip takes 44 minutes
45 minute service only has 1 minute of ‘recovery’ time per round trip
On Time service% is 60-65%, we would like to target 80% plus, as all insights tell us performance is the biggest driver of customer satisfaction
To allow better performance against the plan, ideally we would:
  Add 1 minute in both directions to the schedules
    Results in a 46 minute round trip
    Can operate a 46 minute service if desired
Current financial challenge means increasing the service and operating additional mileage is not likely to be viable
Therefore in current structure it is not possible to deliver requested later services
The proposals for Dec 22 timetable is designed to create repeating patterns on the mainline making connections more reliable and rememberable

## Slide 4: Option 2 – Hourly Frequency
Departure Time |  |  | 05 45 | 06 45 | 07 45 | 08 45 | 09 45 | 10 45 | 11 45 | 12 45 | 13 45 | 14 45 | 15 45 | 16 45 | 17 45 | 18 45 | 19 45 | 20 45 | 21 45 | 22 45
Origin |  |  | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction
Destination |  |  | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey
Watford Junction | dep | 1 | 05 45 | 06 45 | 07 45 | 08 45 | 09 45 | 10 45 | 11 45 | 12 45 | 13 45 | 14 45 | 15 45 | 16 45 | 17 45 | 18 45 | 19 45 | 20 45 | 21 45 | 22 45
Watford North | arr | 2 | 05 48 | 06 48 | 07 48 | 08 48 | 09 48 | 10 48 | 11 48 | 12 48 | 13 48 | 14 48 | 15 48 | 16 48 | 17 48 | 18 48 | 19 48 | 20 48 | 21 48 | 22 48
 | dep | 3 | 05 48 | 06 48 | 07 48 | 08 48 | 09 48 | 10 48 | 11 48 | 12 48 | 13 48 | 14 48 | 15 48 | 16 48 | 17 48 | 18 48 | 19 48 | 20 48 | 21 48 | 22 48
Garston (Hertfordshire) | arr | 4 | 05 51 | 06 51 | 07 51 | 08 51 | 09 51 | 10 51 | 11 51 | 12 51 | 13 51 | 14 51 | 15 51 | 16 51 | 17 51 | 18 51 | 19 51 | 20 51 | 21 51 | 22 51
 | dep | 5 | 05 51 | 06 51 | 07 51 | 08 51 | 09 51 | 10 51 | 11 51 | 12 51 | 13 51 | 14 51 | 15 51 | 16 51 | 17 51 | 18 51 | 19 51 | 20 51 | 21 51 | 22 51
Bricket Wood | arr | 6 | 05 54 | 06 54 | 07 54 | 08 54 | 09 54 | 10 54 | 11 54 | 12 54 | 13 54 | 14 54 | 15 54 | 16 54 | 17 54 | 18 54 | 19 54 | 20 54 | 21 54 | 22 54
 | dep | 7 | 05 54 | 06 54 | 07 54 | 08 54 | 09 54 | 10 54 | 11 54 | 12 54 | 13 54 | 14 54 | 15 54 | 16 54 | 17 54 | 18 54 | 19 54 | 20 54 | 21 54 | 22 54
How Wood | arr | 8 | 05 57 | 06 57 | 07 57 | 08 57 | 09 57 | 10 57 | 11 57 | 12 57 | 13 57 | 14 57 | 15 57 | 16 57 | 17 57 | 18 57 | 19 57 | 20 57 | 21 57 | 22 57
 | dep | 9 | 05 57 | 06 57 | 07 57 | 08 57 | 09 57 | 10 57 | 11 57 | 12 57 | 13 57 | 14 57 | 15 57 | 16 57 | 17 57 | 18 57 | 19 57 | 20 57 | 21 57 | 22 57
Park Street | arr | 10 | 06 00 | 07 00 | 08 00 | 09 00 | 10 00 | 11 00 | 12 00 | 13 00 | 14 00 | 15 00 | 16 00 | 17 00 | 18 00 | 19 00 | 20 00 | 21 00 | 22 00 | 23 00
 | dep | 11 | 06 00 | 07 00 | 08 00 | 09 00 | 10 00 | 11 00 | 12 00 | 13 00 | 14 00 | 15 00 | 16 00 | 17 00 | 18 00 | 19 00 | 20 00 | 21 00 | 22 00 | 23 00
St. Albans Abbey | arr | 12 | 06 02 | 07 02 | 08 02 | 09 02 | 10 02 | 11 02 | 12 02 | 13 02 | 14 02 | 15 02 | 16 02 | 17 02 | 18 02 | 19 02 | 20 02 | 21 02 | 22 02 | 23 02
Service highlighted yellow is the later service we could potentially run subject to agreement with Network Rail Engineering Access

## Slide 5: Option 2 – Hourly Frequency
Departure Time |  |  | 06 08 | 07 08 | 08 08 | 09 08 | 10 08 | 11 08 | 12 08 | 13 08 | 14 08 | 15 08 | 16 08 | 17 08 | 18 08 | 19 08 | 20 08 | 21 08 | 22 08 | 23 08
Origin |  |  | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey
Destination |  |  | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction
St. Albans Abbey | dep | 1 | 06 08 | 07 08 | 08 08 | 09 08 | 10 08 | 11 08 | 12 08 | 13 08 | 14 08 | 15 08 | 16 08 | 17 08 | 18 08 | 19 08 | 20 08 | 21 08 | 22 08 | 23 08
Park Street | arr | 2 | 06 11 | 07 11 | 08 11 | 09 11 | 10 11 | 11 11 | 12 11 | 13 11 | 14 11 | 15 11 | 16 11 | 17 11 | 18 11 | 19 11 | 20 11 | 21 11 | 22 11 | 23 11
 | dep | 3 | 06 11 | 07 11 | 08 11 | 09 11 | 10 11 | 11 11 | 12 11 | 13 11 | 14 11 | 15 11 | 16 11 | 17 11 | 18 11 | 19 11 | 20 11 | 21 11 | 22 11 | 23 11
How Wood | arr | 4 | 06 14 | 07 14 | 08 14 | 09 14 | 10 14 | 11 14 | 12 14 | 13 14 | 14 14 | 15 14 | 16 14 | 17 14 | 18 14 | 19 14 | 20 14 | 21 14 | 22 14 | 23 14
 | dep | 5 | 06 14 | 07 14 | 08 14 | 09 14 | 10 14 | 11 14 | 12 14 | 13 14 | 14 14 | 15 14 | 16 14 | 17 14 | 18 14 | 19 14 | 20 14 | 21 14 | 22 14 | 23 14
Bricket Wood | arr | 6 | 06 17 | 07 17 | 08 17 | 09 17 | 10 17 | 11 17 | 12 17 | 13 17 | 14 17 | 15 17 | 16 17 | 17 17 | 18 17 | 19 17 | 20 17 | 21 17 | 22 17 | 23 17
 | dep | 7 | 06 17 | 07 17 | 08 17 | 09 17 | 10 17 | 11 17 | 12 17 | 13 17 | 14 17 | 15 17 | 16 17 | 17 17 | 18 17 | 19 17 | 20 17 | 21 17 | 22 17 | 23 17
Garston (Hertfordshire) | arr | 8 | 06 20 | 07 20 | 08 20 | 09 20 | 10 20 | 11 20 | 12 20 | 13 20 | 14 20 | 15 20 | 16 20 | 17 20 | 18 20 | 19 20 | 20 20 | 21 20 | 22 20 | 23 20
 | dep | 9 | 06 21 | 07 21 | 08 21 | 09 21 | 10 21 | 11 21 | 12 21 | 13 21 | 14 21 | 15 21 | 16 21 | 17 21 | 18 21 | 19 21 | 20 21 | 21 21 | 22 21 | 23 21
Watford North | arr | 10 | 06 23 | 07 23 | 08 23 | 09 23 | 10 23 | 11 23 | 12 23 | 13 23 | 14 23 | 15 23 | 16 23 | 17 23 | 18 23 | 19 23 | 20 23 | 21 23 | 22 23 | 23 23
 | dep | 11 | 06 23 | 07 23 | 08 23 | 09 23 | 10 23 | 11 23 | 12 23 | 13 23 | 14 23 | 15 23 | 16 23 | 17 23 | 18 23 | 19 23 | 20 23 | 21 23 | 22 23 | 23 23
Watford Junction | arr | 12 | 06 25 | 07 25 | 08 25 | 09 25 | 10 25 | 11 25 | 12 25 | 13 25 | 14 25 | 15 25 | 16 25 | 17 25 | 18 25 | 19 25 | 20 25 | 21 25 | 22 25 | 23 25
Service highlighted yellow is the later service we could potentially run subject to agreement with Network Rail Engineering Access

## Slide 6: Option 3 – Hybrid
Departure Time |  |  | 05 45 | 06 30 | 07 15 | 08 00 | 08 45 | 09 45 | 10 45 | 11 45 | 12 45 | 13 45 | 14 45 | 15 45 | 16 30 | 17 15 | 18 00 | 18 45 | 19 45 | 20 45 | 21 45 | 22 45
Origin |  |  | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction
Destination |  |  | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey
Watford Junction | dep | 1 | 05 45 | 06 30 | 07 15 | 08 00 | 08 45 | 09 45 | 10 45 | 11 45 | 12 45 | 13 45 | 14 45 | 15 45 | 16 30 | 17 15 | 18 00 | 18 45 | 19 45 | 20 45 | 21 45 | 22 45
Watford North | arr | 2 | 05 48 | 06 33 | 07 18 | 08 03 | 08 48 | 09 48 | 10 48 | 11 48 | 12 48 | 13 48 | 14 48 | 15 48 | 16 33 | 17 18 | 18 03 | 18 48 | 19 48 | 20 48 | 21 48 | 22 48
 | dep | 3 | 05 48 | 06 33 | 07 18 | 08 03 | 08 48 | 09 48 | 10 48 | 11 48 | 12 48 | 13 48 | 14 48 | 15 48 | 16 33 | 17 18 | 18 03 | 18 48 | 19 48 | 20 48 | 21 48 | 22 48
Garston (Hertfordshire) | arr | 4 | 05 50 | 06 35 | 07 20 | 08 05 | 08 50 | 09 51 | 10 51 | 11 51 | 12 51 | 13 51 | 14 51 | 15 50 | 16 35 | 17 20 | 18 05 | 18 51 | 19 51 | 20 51 | 21 51 | 22 51
 | dep | 5 | 05 51 | 06 36 | 07 21 | 08 06 | 08 51 | 09 51 | 10 51 | 11 51 | 12 51 | 13 51 | 14 51 | 15 51 | 16 36 | 17 21 | 18 06 | 18 51 | 19 51 | 20 51 | 21 51 | 22 51
Bricket Wood | arr | 6 | 05 54 | 06 39 | 07 24 | 08 09 | 08 54 | 09 54 | 10 54 | 11 54 | 12 54 | 13 54 | 14 54 | 15 54 | 16 39 | 17 24 | 18 09 | 18 54 | 19 54 | 20 54 | 21 54 | 22 54
 | dep | 7 | 05 54 | 06 39 | 07 24 | 08 09 | 08 54 | 09 54 | 10 54 | 11 54 | 12 54 | 13 54 | 14 54 | 15 54 | 16 39 | 17 24 | 18 09 | 18 54 | 19 54 | 20 54 | 21 54 | 22 54
How Wood | arr | 8 | 05 56 | 06 41 | 07 26 | 08 11 | 08 56 | 09 57 | 10 57 | 11 57 | 12 57 | 13 57 | 14 57 | 15 56 | 16 41 | 17 26 | 18 11 | 18 57 | 19 57 | 20 57 | 21 57 | 22 57
 | dep | 9 | 05 56 | 06 41 | 07 26 | 08 11 | 08 56 | 09 57 | 10 57 | 11 57 | 12 57 | 13 57 | 14 57 | 15 56 | 16 41 | 17 26 | 18 11 | 18 57 | 19 57 | 20 57 | 21 57 | 22 57
Park Street | arr | 10 | 05 59 | 06 44 | 07 29 | 08 14 | 08 59 | 10 00 | 11 00 | 12 00 | 13 00 | 14 00 | 15 00 | 15 59 | 16 44 | 17 29 | 18 14 | 19 00 | 20 00 | 21 00 | 22 00 | 23 00
 | dep | 11 | 05 59 | 06 44 | 07 29 | 08 14 | 08 59 | 10 00 | 11 00 | 12 00 | 13 00 | 14 00 | 15 00 | 15 59 | 16 44 | 17 29 | 18 14 | 19 00 | 20 00 | 21 00 | 22 00 | 23 00
St. Albans Abbey | arr | 12 | 06 01 | 06 46 | 07 31 | 08 16 | 09 01 | 10 02 | 11 02 | 12 02 | 13 02 | 14 02 | 15 02 | 16 01 | 16 46 | 17 31 | 18 16 | 19 02 | 20 02 | 21 02 | 22 02 | 23 02
Service highlighted yellow is the later service we could potentially run subject to agreement with Network Rail Engineering Access

## Slide 7: Option 3 – Hybrid
Departure Time |  |  | 06 07 | 06 52 | 07 37 | 08 22 | 09 08 | 10 08 | 11 08 | 12 08 | 13 08 | 14 08 | 15 08 | 16 07 | 16 52 | 17 37 | 18 22 | 19 08 | 20 08 | 21 08 | 22 08 | 23 08
Origin |  |  | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey | St. Albans Abbey
Destination |  |  | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction | Watford Junction
St. Albans Abbey | dep | 1 | 06 07 | 06 52 | 07 37 | 08 22 | 09 08 | 10 08 | 11 08 | 12 08 | 13 08 | 14 08 | 15 08 | 16 07 | 16 52 | 17 37 | 18 22 | 19 08 | 20 08 | 21 08 | 22 08 | 23 08
Park Street | arr | 2 | 06 10 | 06 55 | 07 40 | 08 25 | 09 11 | 10 11 | 11 11 | 12 11 | 13 11 | 14 11 | 15 11 | 16 10 | 16 55 | 17 40 | 18 25 | 19 11 | 20 11 | 21 11 | 22 11 | 23 11
 | dep | 3 | 06 10 | 06 55 | 07 40 | 08 25 | 09 11 | 10 11 | 11 11 | 12 11 | 13 11 | 14 11 | 15 11 | 16 10 | 16 55 | 17 40 | 18 25 | 19 11 | 20 11 | 21 11 | 22 11 | 23 11
How Wood | arr | 4 | 06 12 | 06 57 | 07 42 | 08 27 | 09 14 | 10 14 | 11 14 | 12 14 | 13 14 | 14 14 | 15 14 | 16 12 | 16 57 | 17 42 | 18 27 | 19 14 | 20 14 | 21 14 | 22 14 | 23 14
 | dep | 5 | 06 13 | 06 58 | 07 43 | 08 28 | 09 14 | 10 14 | 11 14 | 12 14 | 13 14 | 14 14 | 15 14 | 16 13 | 16 58 | 17 43 | 18 28 | 19 14 | 20 14 | 21 14 | 22 14 | 23 14
Bricket Wood | arr | 6 | 06 15 | 07 00 | 07 45 | 08 30 | 09 17 | 10 17 | 11 17 | 12 17 | 13 17 | 14 17 | 15 17 | 16 15 | 17 00 | 17 45 | 18 30 | 19 17 | 20 17 | 21 17 | 22 17 | 23 17
 | dep | 7 | 06 15 | 07 00 | 07 45 | 08 30 | 09 17 | 10 17 | 11 17 | 12 17 | 13 17 | 14 17 | 15 17 | 16 15 | 17 00 | 17 45 | 18 30 | 19 17 | 20 17 | 21 17 | 22 17 | 23 17
Garston (Hertfordshire) | arr | 8 | 06 18 | 07 03 | 07 48 | 08 33 | 09 20 | 10 20 | 11 20 | 12 20 | 13 20 | 14 20 | 15 20 | 16 18 | 17 03 | 17 48 | 18 33 | 19 20 | 20 20 | 21 20 | 22 20 | 23 20
 | dep | 9 | 06 19 | 07 04 | 07 49 | 08 34 | 09 21 | 10 21 | 11 21 | 12 21 | 13 21 | 14 21 | 15 21 | 16 19 | 17 04 | 17 49 | 18 34 | 19 21 | 20 21 | 21 21 | 22 21 | 23 21
Watford North | arr | 10 | 06 21 | 07 06 | 07 51 | 08 36 | 09 23 | 10 23 | 11 23 | 12 23 | 13 23 | 14 23 | 15 23 | 16 21 | 17 06 | 17 51 | 18 36 | 19 23 | 20 23 | 21 23 | 22 23 | 23 23
 | dep | 11 | 06 21 | 07 06 | 07 51 | 08 36 | 09 23 | 10 23 | 11 23 | 12 23 | 13 23 | 14 23 | 15 23 | 16 21 | 17 06 | 17 51 | 18 36 | 19 23 | 20 23 | 21 23 | 22 23 | 23 23
Watford Junction | arr | 12 | 06 23 | 07 08 | 07 53 | 08 38 | 09 25 | 10 25 | 11 25 | 12 25 | 13 25 | 14 25 | 15 25 | 16 23 | 17 08 | 17 53 | 18 38 | 19 25 | 20 25 | 21 25 | 22 25 | 23 25
Service highlighted yellow is the later service we could potentially run subject to agreement with Network Rail Engineering Access

## Slide 8: Southbound Watford Junction Connections
Departure Time | Destination | Fast Line/Slow Line
Xx:12 | London Euston | Slow Line
Xx:28 | London Euston | Slow Line
Xx:33 | London Euston | Fast Line
Xx:42 | London Euston | Slow Line
Xx:58 | London Euston | Slow Line
Arrival time from Abbey Line | Connection Time to Euston Service
Xx:23 | 5 mins
Xx:38 | 20 mins
Xx:53 | 5 mins
Xx:08 | 20 mins
45 minute service
A repeating 45 minute service results in 4 different possible arrival times, and therefore different connection times with the hourly service
Arrival time from Abbey Line | Connection Time to Euston Service
Xx:25 | 8 mins
Hourly service always has an 8 minute connection at Watford with the Fast Line service to Euston
Hourly service
This slide shows the connections if a passenger was travelling to London Euston from the Abbey Line. The departure times at Watford from Euston are shown below and compared with arrivals from St Albans Abbey in both a 45 minute structure and an hourly structure

## Slide 9: Northbound Watford Junction Connections
Time | Origin | Fast Line/Slow Line
Xx:12 | London Euston | Slow Line
Xx:29 | London Euston | Slow Line
Xx:37 | London Euston | Fast Line
Xx:42 | London Euston | Slow Line
Xx:59 | London Euston | Slow Line
This slide shows the connections if a passenger was travelling from London Euston wanting to access the Abbey Line. The arrival times at Watford from Euston are shown below and compared with departures to St Albans Abbey in both a 45 minute structure and an hourly structure
Departure time to Abbey Line | Connection Time to Euston service
Xx:00 | 18 mins
Xx:15 | 16 mins
Xx:30 | 18 mins
Xx:45 | 8 mins
Departure time to Abbey Line | Connection Time to Euston Service
Xx:45 | 8 mins
45 minute service
Hourly Service

## Slide 10: Southbound Watford Junction Connections
Arrival Time | Origin | Fast Line/Slow Line
Xx:11 | Milton Keynes Central | Slow Line
Xx:27 | Tring | Slow Line
Xx:31 | Birmingham New Street | Fast Line
Xx:41 | Milton Keynes Central | Slow Line
Xx:57 | Tring | Slow Line
This slide shows the connections if a passenger was travelling to the Abbey Line wanting from Milton Keynes Central or beyond. The arrival times at Watford from the north are shown below and compared with departures to St Albans Abbey in both a 45 minute structure and an hourly structure
Departure time to Abbey Line | Connection Time from MKC Service
Xx:00 | 19 mins
Xx:15 | 18 mins
Xx:30 | 19 mins
Xx:45 | 14 mins
45 minute service
A repeating 45 minute service results in 4 different possible departure times, and therefore different connection times with the hourly service
Departure time to Abbey Line | Connection Time from MKC Service
Xx:45 | 14 mins
Hourly service always has an 14 minute connection at Watford from the fast service from Milton Keynes Central
Hourly service

## Slide 11: Northbound Watford Junction Connections
Time | Destination | Fast Line/Slow Line
Xx:13 | Tring | Slow Line
Xx:30 | Milton Keynes Central | Slow Line
Xx:38 | Birmingham New Street | Fast Line
Xx:43 | Tring | Slow Line
Xx:00 | Milton Keynes Central | Slow Line
This slide shows the connections if a passenger was travelling from the Abbey Line wanting to travel north towards Milton Keynes Central. The departure times at Watford to the north are shown below and compared with arrivals from St Albans Abbey in both a 45 minute structure and an hourly structure
Arrival time from Abbey Line | Connection Time to Service calling at Milton Keynes
Xx:23 | 15 mins*
Xx:38 | 22 mins
Xx:53 | 7 mins
Xx:08 | 22 mins
*7 minute connection available, but service is overtaken by the 15 minute connection option
Arrival time from Abbey Line | Connection Time to Euston Service
Xx:25 | 13 mins
45 minute service
Hourly Service

## Slide 12: Appendix

## Slide 13: Transport Focus Survey
Punctuality by far the biggest driver of satisfaction according to the National Rail Passenger Survey